## Slide 1
Introduction
STATISTICAL ANALYSIS OF URBAN AIR QUALITY IN PLOIESTI, ROMANIA DURING AUTUMN
Georgeta O. Popa1,2, Cristian Constantin1,2, Simona M. Calinescu1,*
1National Research and Development Institute for Industrial Ecology ECOIND, Drumul Podu Dambovitei Street, No. 57-73, ZIP Code 060652, Bucharest, Romania
2Faculty of Chemical Engineering and Biotechnologies, University Politehnica of Bucharest, 1-7, Gheorghe Polizu Street, Sector 1, ZIP Code 011061 Bucharest, Romania
*poluare.aer@incdecoind.ro
Air pollutant emissions and weather conditions contribute to urban air quality. In this study, we statistically investigated data collected on urban air pollution using air quality monitoring station measurements. Long-term monitored pollutants were PM10, SO2, NO2, CO and meteorological parameters from 01.09.2023-30.11.2023 in Ploiesti, Romania.
SICHEM
2024
Introduction
Method of analysis
Data were processed according to the limit value allowed under the Romanian environmental legislation (LAW no. 104 of 15 June 2011 on ambient air quality). Correlations were made between weather parameters and pollutant concentrates. They were then statistically analyzed. Ploiesti municipality includes 2 stations for monitoring emissions from traffic, 2 background stations and 1 stations for monitoring industrial emissions (Fig. 1).
Results and discussions
The most significant exceedance is for PM10 with a percentage of 59.54% compared to the permissible limit value (PLV), Fig.2.
Weather data were statistically analyzed with the Aermet View program to eliminate aberrant values and obtain wind distribution over a three-month period, indicating the prevailing „blowing from” from NV and SV, most winds having a speed between 0.5-2.1 m/s and about 62% of the monitored period were characterized by atmospheric calm, and higher intensity winds are present in only 0.2% of the time (Fig. 3).
Fig. 4 shows daily concentrations of pollutants over time as box plots diagrams. The graphical representation illustrates the minimum value, the lower quartile, the upper median quartile and the maximum value. Extreme values are predominantly found in November. For nitrogen dioxide (NO2), the average concentration decrease in September for the PH-6 station is the highest compared to the other two monitoring stations (55.01%). In the analysis of the concentration of particulate matter for PH-5 with an aerodynamic diameter of 10 micrometers (PM10) we find a slight decrease for October compared to September, after that followed an upward trend for November, with a percentage increase of 37.59%. These fluctuations are due to the density of road traffic, meteorological parameters, vehicle types and industrial emissions.
Figure 1. Localization of air quality monitoring stations in Ploiesti municipality
Figure 4. Statistical summary of the level of air pollution in the form of box plants in September, October, November of CO, NO2, SO2 and PM10
Concentration of NO2, , µg/m³
September October November
Concentration of PM10, , µg/m³
September October November
Concentration of CO , mg/m³
September October November
Figure 3. The wind rose specific to the area and the monitoring period
Conclusion
The emission of air pollutants is influenced by various factors such as: the chemical changes that occur with their emission in atmospheric air, the interaction with solar radiation, the dispersion in the atmosphere (wind direction, wind speed) and weather.
The variation of emissions in urban areas on several factors, such as: road traffic, vehicle type, fuel used, pollution reduction measures, average speed, traffic congestion degree.
The study highlights the crucial importance of addressing air pollution due to road transport in metropolitan areas in Romania.
2023
2023
2023
2023
Chart: SEPTEMBER
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
PH-1 | 13.63 | 12.72 | 9.27 | 10.9 | 13.08 | 12.72 | 0 | 15.99 | 18.71 | 21.8 | 23.25 | 27.07 | 29.98 | 29.25 | 28.16 | 16.9 | 19.8 | 21.26 | 24.89 | 25.44 | 25.25 | 26.71 | 28.34 | 22.17 | 25.07 | 25.62 | 24.89 | 25.44 | 25.07 | 27.43
PH-2 | 11.45 | 12.36 | 9.63 | 11.08 | 14.72 | 14.72 | 15.26 | 16.17 | 14.17 | 18.9 | 20.53 | 27.07 | 30.89 | 28.89 | 25.26 | 17.99 | 19.44 | 18.35 | 20.71 | 23.8 | 24.35 | 26.89 | 32.34 | 21.26 | 27.25 | 34.16 | 31.8 | 26.35 | 25.8 | 25.44
PH-3 | 17.81 | 5.27 | 9.81 | 15.63 | 45.97 | 19.81 | 21.99 | 22.9 | 18.35 | 23.08 | 25.26 | 32.71 | 33.8 | 34.71 | 27.62 | 19.44 | 25.26 | 25.8 | 25.62 | 26.17 | 28.89 | 30.89 | 37.98 | 29.07 | 64.51 | 79.77 | 61.23 | 47.24 | 47.79 | 29.07
PH-6 | 15.99 | 23.08 | 14.35 | 11.63 | 16.72 | 16.53 | 15.99 | 19.44 | 11.63 | 11.99 | 17.08 | 25.07 | 29.8 | 29.44 | 27.26 | 30.35 | 25.8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 22.17 | 18.17 | 18.71 | 23.8
VLA µg/m³ conf. Legea 104/2011 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
PLV LAW 104/2011
Figure 2. Daily variation in PM10 concentration
Ploiesti municipality